Using Vision, CyberSynth, and AMIII

1)	Someone had turned down the volume in the Control Strip in Studio 1, which is why we did not hear

CyberSynth being played manually.  I removed the Control Strip sound module.

2)	In order to avoid confusing Sound Manager, do not make any changes to sound in the Control Panel

"Monitors and Sound".

3)	Use the Sound Control Panel located in the Configurations submenu of the Apple Menu, as we have

been doing.

4)	To use Sound Designer and Protools, set the Sound Out to Built In, then launch the desired application.

5)	To use Vision with CyberSynth only (sending CyberSynth to the Digidesign card), do the following:

a)	Set Sound Out to Built In (yes, that's right)

b)	Launch Vision

c)	Pull down the Audio Menu, access the Audio System submenu, and select MIDI only.

d)	Quit Vision (you do not have to save).

e)	Set Sound Out to Digidesign

f)	Launch Vision and do your assignment.  No digital audio will be possible in this mode.

6)	To use Vision with digital audio, either alone or with CyberSynth, do the following:

a)	Set Sound Out to Built In

b)	Launch Vision

c)	Pull down the Audio Menu, access the Audio System submenu, and select DAE.

d)	Proceed with your work.  Note that digital sound is sent to AMIII and CyberSynth

is sent to Mac out in the patch bay.

Please remember to sign in.