## Composition: Electronic Media I

Sept. 21, 2005

Filtering in Pro Tools

1.	The following filtering technologies will be discussed in class:

- Bass, Treble, Midrange boost/cut knobs on mixers, home stereo, guitar amplifiers, and other commercial uses.

- Classic Filter (see Allis0n in class)

- Graphic Equalizer, (see B and K in class)

- Voltage-controlled filter (see Moog Synthesizer in class)

- Software EQ, see Pro Tools discussion below.

2.	Basic Filter Theory:

Source sound passes through a filter.  The filter attenuates (reduces, cuts, rejects) selected frequencies, passes selected frequencies unaltered, or boosts (increases, amplifies) selected frequencies.

3.	Compositional uses of filters:

- To clean up a sound, by removing rumbling bass, heavy midrange, piercing highs, etc.

- To modify, in a somewhat crude way, the timbre of a sound, making a dark sound light, and a light sound dark.

- To isolate a single sound from a complex signal for later compositional manipulation.

4.	 Types of Filters:

- Band Pass: .  Low fequencies are attenuated, middle frequencies are flat (passed, unaltered), and high frequencies are attenuated.  Note the cut-off frequencies, Q (width of the band-pass), amplitude (or gain) of the band-pass, and center frequency.  In Waves, this situation will be a little different, as discussed in class.

- Band Reject:  This is the vertical inverse of the Band Pass Filter.  Here, the Q represents the width of the band reject.  In Waves, the Band-Pass function is often used as a band-reject function, as discussed in class.

- Low Pass: . High frequencies are attentuated above a cut-off frequency.  In Waves, any filter plug-in can do this.

- High Pass: . Low frequencies are attentuated below a cut-off frequency.  In Waves, any filter plug-in can do this.

- High Shelf: . High frequencies are boosted above a cut-off frequency.  Compare to High Pass.

- Low Shelf: . Low frequencies boosted above a cut-off frequency.  Compare to Low Pass.

5.	To use a filter in Pro Tools, do the following:

- Launch Pro Tools and import a mono or stereo sound, placing it in the edit window.

- Highlight the sound, then select AudioSuite>EQ>Q10 stereo or mono, as shown below:

5. c.	A window like the one below will appear:

Note the following controls and function:

Load, Save, Flat:

Graphic Frequency/Time/Amplitude Window:

Input:

On/Off:

Type:

Gain:

Freq:

Q:

Output Sliders:

Output Meters:

Peak Indicators above Output Meters: