# Composition: Electronic Media I

Fritts

# Fall 2004

# SoundHack Overview

1)	The File menu displays the following functions:

a)	Record New: used for recording a mic/line signal through the Mac input.

b)	Open:  Opens standard audio files.  You can also drag and drop these files onto the  SoundHack icon.

c)	Open Any:  Opens unusal or headless files, sometimes with interesting results.

d)	Close:  Close any selected open file.

e)	Split Into Mono Files:  Splits a stereo interleaved file into 2 mono files.

f)	Import: Snd Resource (Games), CD track.

2)	The Edit menu does not appear to be useful.

3)	The Hack menu displays the following functions:

- Binaural Filter:  Used to stereoize mono files according to vertical and horizontal placement of source relative to ear.  Fixed angle or moving angle possible.

- Convolution:  Discussed below.

- Spectral Dynamics:

- Mutation

- Phase Vocoder

- Varispeed

- Spectral Extractor

- Normalize

4)	To use the convolution function, do the following:

- Open any soundfile you wish to convolve.

- Select Hack>Convolution

- A dialog like the one below will appear:

- Select the options shown above, then click on “Pick Impulse”.

- An open dialog will appear.  Select a very short soundfile to use as an impulse.

- Click on “Process”.

- A new file will be created named “file1 * file2”.

5)	To use the Phase Vocoder, do the following:

- Open any soundfile you wish to transform in pitch or time.

- Select Hack>Phase Vocoder

c)	A dialog like the ones below will appear:

d)	The dialog settings shown on the left will transpose the pitch of the soundfile up 14 semitones (-14 will transpose down).

e)	The dialog settings shown on the right will time stretch the soundfile to 20 times its original length.