# Composition: Electronic Media II

Feb. 1, 2006

Live Spectral Analysis in Kyma

1.	Plugging in a mic signal:

a)	Plug the Shure SM57 into the xlr mic cable.

b)	Plug the cable into the back of the Capybara Analog In 1.

c)	Select from the menu DSP>Status.  A window like the one below will appear:

Leave the values where they are.  Note that the mic signal is displayed

In the upper left meter.

d)	Close the DSP Status window when you are done.

2.	Create a new Sound File and do the following:

a)	Drag and drop the PolyphonicPitchShift Resynth LITE prototype (found in the Spectral Processing-Live     	category) into the Sound File.  Double-click on the Sound and open all of its tails, as shown below:

b)	Double-click on PolyphonicPitchShift ResynthLITE.  An edit window like the one below will appear:

Set the values to those shown above.  Discussion of NbrOscillators.

c)	Double-click on nonharmonic Analysis.  An edit window like the one below will appear:

Set the values to those shown above.

d)	Double-click on GenericSource.  A window like the one below will appear:

Set the values to those shown above.

e)	Compile from PolyphonicPitchShift ResynthLITE.  A Virtual Control Surface like the one below will appear:

Sing into the mic and adjust the pitch with the Interval1 slider.

3.	To use a MIDI File to control the frequency of the live input, do the following:

a)	Acquire a MIDI File and place it on the desktop.

b)	Drag and drop a MIDIMapper Prototype between the PolyphonicPitchShift ResynthLITE and the speaker

icon, as shown below:

c)	Double-click on MIDIMapper.  A window like the one below will appear:

Set the values to those shown above.

d)	Double-click on nonharmonicAnalysis.  A window like the one below will appear:

Set the values to those shown above.

e)	Compile from the MIDIMapper and start singing.  Or hold one tone and let the MIDI File do the singing for 		you.