025:251 COMPOSITION: ELECTRONIC MEDIA II

Assignment 2

Due Wednesday, Feb. 12

Part 1

Purpose:  To use Vision and CyberSynth instruments to generate soundfiles to be used as possible source

material for your compositions.

Material:	30' or 60' DAT tape.

1)	Create at least 6 Vision sequences according to the following specifications:

a)	each sequence should have at least 4 MIDI tracks sent to CyberSynth Drivers 1, 2, ...

b)	each sequence should consist of a series of at least 8 fragments separated by one bar of silence.

c)	fragments within a sequence should be variations of the same type (same patches, same texture)

d)	a fragment's texture may be (1) a short or long chord; (2) a contrapuntal texture (parallel, nonparallel;

rhythmically interlocking, poly, serial, or free; ascending, descending, mixed, static); (3) pointillistic; 		(4) clouds or washes; (5) bucket of bolts spilled onto floor; (6) etc.

e)	all registers should be represented in the assignment

f)	a range of CyberSynth families (pitched perc, nonpitched perc, winds, brass, organ/synth, pluck, etc.)

should be represented in the assignment.

g)	use of volume and pitchbend is optional.

2)	Record the Vision sequences digitally from the AMIII to a 30-60' DAT.

Part 2

Purpose:	To apply envelopes to the Kyma Sounds created in Assignment 2.

1)	Send every sound source (diskplayer, samples, carrier oscillators, modulator oscillators) to a VCA

prototype whose inputs are:

a)	the original source or a filtered (or granulated, reverbed, etc) version of it.

b)	an ADSR envelope.

2)	Note that when VCA prototype is added to the signal chain to the right of the source, you will be

asked whether you want ADSR or samples to be replaced by your source.  Keep ADSR and

replace samples with your source.

3)	Use hot parameters, type in values, or both for the following ADSR parameter fields:

a)	attack

b)	decay

c)	sustain

d)	release

4)	Every ADSR in your sound should use !KeyDown in the Gate parameter field (this will trigger the

envelopes).

5)	Experimentalists may wish to use MultiSegmentEnvelope to control the PitchBend parameter field of

any oscillators, either carrier or modulators.

6)	Experimentalists may also replace any ADSR envelope with a MultiSegmentEnvelope.

Part 3

Purpose:	To created composite sounds by using envelopes to crossfade between several individual sounds.

1)	Create a new Sound with a Mixer prototype.

2)	Use any of your enveloped Sounds as inputs to the mixer.

3)	Create other enveloped Sounds, such as filtered noise, and use these as inputs also.

4)	Insert a TimeOffSet prototype between each ADSR and its VCA.

5)	Use a unique set of values (using hot parameters, typing, or both) for each envelope and a unique

SilentTime value for TimeOffSet , so that the overall sound crossfades and/or mixes between the 	individual sounds.  Remember to use !KeyDown for every envelope's Gate.

Readings for Monday

Review of Peavey PC1600 in Electronic Musician, March 1993, Vol. 9, No. 3, pp. 113-115.

Review of Opcode Studio Vision Pro 3.0 in Electronic Musician, April 1996, Vol. 12, No. 4, pp. 112-123.

(Don't worry about SMPTE or syncing machines).

"Persistence of Vision" in Electronic Musician, Oct. 1996, Vol. 12, No. 10, pp. 70-85.

Vision Presentations for Monday

____________________________	Using tempo track

____________________________	Using meter track

____________________________	Moving pitches in Graphic window

____________________________	Moving pitches in Notation window

____________________________	Transposing pitches in Notation window

____________________________	Changing pitch duration in Notation window

____________________________	Changing patches in a track in List window

____________________________	Copying tracks from one sequence to another

Consult the Studio Vision MIDI Reference Manual for details.