025:251 COMPOSITION: ELECTRONIC MEDIA II

Assignment 5

Due Wed. April 7

Purpose:  To do create, play, and record spectral files in Kyma.

1)	Patch the Capybara into the audio system and turn it on.  Make sure the Mac monitors are set to 256 	colors.

2)	Create a folder on the Scratch disk titled, "YI.Spectral".  Place into this folder copies of the following:

a)	Larry's Kyma module named "LF.SOS".

b)	Any of your cells and transformations from Assignment 3.  These must be in SDII or aiff format and

mono.

c)	Make sure that all files and saves you do during this assignment are saved to this folder.

3)	Launch Kyma.

4)	Create a spectral analysis of one of your files, "YI.Cell.1", as follows:

a)	Select Tools>Spectral Analysis.  A window like the one below will appear:

b)	Click "Select" and navigate through the dialog box to find "YI.Cell.1".

c)	Click "Next".  A window like the one below will appear:

d)	Follow the instructions in the window.  Click "Audition" to hear the analyzed result.

When satisfied, click "Next".  A window like the one below will appear:

e)	Click "Create Spectrum File".  You will be prompted to save a spectral file named

"YI.Cell.1 s256".  Make sure that you save to your "YI.Spectral" folder.

f)	After saving, an untitled window containing "YI.Cell.1 s256" as an SOS module will appear.  Since 		this module is not needed, close the window.

g)	Click "EXIT" on the Spectral Analsis window.

5)	Repeat Step 4 to create spectral files of your other cells or transformations.

6)	Open the soundfile "LF.SOS" from the main menu.  The flow chart for this sound is shown

below:

7)	See Assignment 4 for an overview of Diskrecorder and MIDIMapper.

8)	Notice the parameters settings for the SOS sound, as show below:

9)	To select your spectral files "YI.Cell.1 s 256" and "YI.Cell.2 s 256" do the following:

a)	Click on the disk icon for Analysis0 and navigate throught the dialog box to select "YI.Cell.1 s 256".

b)	Click on the disk icon for Analysis1 and navigate throught the dialog box to select "YI.Cell.2 s 256".

10) Notice the parameter settings for ADSR, as shown below:

11) Notice how the hot parameters appear in the Virtural Control Surface.

12) Play your spectral files from your choice of the Fatar keyboard, Peavey, or Vision.  Record these

performances to disk (see Assignment 4), and edit in Sound Designer.

13) Bring @30 seconds of SDII files of these performances to class on Wed. April 7.  Place them on the

Scratch disk before class.