## Composition: Electronic Media II

Feb. 6, 2006

Intro to MIDI

1.		History and premises of MIDI (Musical Instrument Digital Interface).

a.	Dave Smith, 1982

b.	Communication protocol between digital instruments produced by different manufacturers.

c.	Event-oriented.

d.	General MIDI

2.		The downside of MIDI:

a.	Latency

b.	Log jams

c.	Event-oriented

d.	General MIDI

3.	MIDI Plug

Note the 5 pins

4.	MIDI Plug anatomy:

Note the 3 wires.

5.		MIDI jacks: in, out, thru

6.	Basic MIDI set-up:

7.	Expanded MIDI set-up:

8.	MIDI devices in EMS:

a.	Fatar Keyboard

b.	Peavey PC-1600 faders

c.	Foot volume controls

d.	MOTU MIDI Patch Bay

9.	Other types of MIDI devices that we can buy?

10.	Basics of MIDI transmission:

a.	UART: Universal Asynchronous Receiver/Transmitter

b.	UART sends and receives high and low voltages.  High voltage interpreted as 0 and low voltage interpreted as 1 in binary 				code.

c.	Baud rate = 31,250 bits per second

d.	Bit: 1 digit, 0 or 1, base 2.

6.	Discussion of base 2:

a.	0000 base 2 = 0 base 10

b.	0001 base 2 = 1 base 10

c.	0010 base 2 = 2 base 10

d.	0011 base 2 = 3 base 10

7.	More on MIDI transmission.

a.	Data stream

b.	10-bit chunk

c.	start and stop bits

d.	8-bit data byte.

8.	Basics of MIDI Messages:

a.  	Status Byte: Most Significant Bit (MSB) = 1

b.	Data Byte: Most significant Bit (MSB) = 0

9.	Status Byte:

| y | y | y | x | x | x | x | Start = 1 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type of Data Messages to follow | Channel message |  |
| Note off | Ch. 1-16 |  |
| Note on | Ch. 1-16 |  |
| Polyphonic | Ch. 1-16 |  |
| Aftertouch | Ch. 1-16 |  |
| Control Change (continuous controller) | Ch. 1-16 |  |
| Program Change | Ch. 1-16 |  |
| Channel Aftertouch | Ch. 1-16 |  |
| System | Ch. 1-16 |  |
| Note: 2^3 = 8 | Note: 2^4 = 16 |  |

10.First Data Byte:

| y | y | y | x | x | x | x | Start = 0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Note: 2^7 = 128 |  |

Note off = 0 - 127

Note on = 0 - 127

Control Change = 0 – 127

Program Change = 0 – 127

11. If  the first Data Byte is note on or off, then a second Data Byte follows:

a. 	velocity

b.	0 – 127

c.	Back in the day story.