## Composition: Electronic Media II

Spring 2009

Building a Patch in Max/MSP

1.	Power up the studio and bring up the faders to the Digi and Mac.

2.	Launch Max/MSP by clicking on the Max icon in the dock, as shown below:

3.	Select File>New Patcher to create a new patch.  A window like the one below will appear:

4.	Double-click in the lower middle area of the window.  A target like the one below will appear:

5.	In the object palette, click on the object icon.  An empty object object like the one below will appear:

6.	Type “dac~”, as shown below:

Notice the following:

- “dac” stands for digital to analog converter.  It converts digital sounds into analog audio sounds.

- The ~ (tilde) sign indicates that the object is an audio or MSP object.

- The dac~ object has a left audio inlet and a right audio inlet.

- You can make the object box longer by grabbing the right side and resizing.

7.	Using a similar procedure, insert a toggle object and patch it into the left inlet of the dac~, as shown below:

Notice the following:

1.	The dac~ needs to be turned on and off.  The toggle will accomplish this.

2.	This is a segmented patch cord (see the options menu).

3.	The patch cord is a plain, black line, which indicate that it is a control signal, not audio.

8.	Using a similar procedure, insert an object object directly above the dac~ and patch it into its left inlet of the dac~, as shown below:

As shown above, type “*~ 0.5” into the box.  This is now called a “signal multiplier” object.

9.	Patch the signal multiplier object into the right inlet of the dac~, as shown below:

Notice the following:

- The Signal Multiplier will be used to control the volume of the left and right channels of the dac~.

- The patch cords are dashed, yellow and black lines, which indicate that these are audio signals, not control signals.

10.	Using a similar procedure, insert a float number box above and to the right of the signal multiplier, as shown below:

As shown above, patch it into the right inlet of the signal multiplier.

Notice the following:

- The Float Number Box will be used to supply a decimal number to the Signal Multiplier.

- This decimal number will function as a volume control for the dac~.

11.	Using a similar procedure, insert a message box directly above the signal mulitplier and type “cycle~ 440”, as shown

below:

Notice the following:

1.	The cycle~ object is a sine wave.

2.	The patch cord is an audio signal.

12.	 Play the patch as follows:

a)	 Lock the Patcher.

- Click on the toggle.

c)	Adjust the volume from the Float Box.

d)	Press “stop” to stop the sound.

13.	To learn more about the cycle~ object, unlock the patcher, highlight cycle~  and type cmd-shift-h.  A window like the

one below will appear:

Note the following:

a)	 Most objects have similar help windows.

- Items from a help window can be unlocked, copied, and pasted.

- Each item from a help window also has its own help window, accessed by typing cmd-shift-h as above.

- Beware of running multiple dac~s.

14.  How about controlling the frequency from a number box?

15. Save, name, and store the patch, then quit Max/MSP.